## Slide 1: Systems Modelling and Simulation (Lab session 8)
A. Mousavi
After this session you should understand
Modelling multiple process plans for different parts.
More on entity transfer

## Slide 2: Overview of Entity Transfer Types
Entity Transfer
Types
Connectors
Routes
And
Stations
Resource-
Constrained
Transfer
Transporters:
Multi-
Directional
Conveyors:
Normally
Unidirectional
Free Path
Transporters:
Ignores traffic
Guided
Transporters:
Affected by
traffic
Non-
accumulating
Conveyors:
Stops and
Starts for
Access and Exit
Accumulating
Conveyors:
Never stops

## Slide 3: Entity Transfer types so far
Connect – No Delay
Routes
  Delay
  Direct route or entity sequence
  Limit less
Entities move along system by themselves

## Slide 4: New Entity Transfer Type
Resource-constrained transfers
  Limit total number of entities in transit at a time
  Examples: Health care (Patients walk-in), Telecommunications (number of packets), Logistics (number of vehicles)
Material-handling devices
  Transporters (multi-Directional)
  Examples: AGVs, fork lifts, trucks, carts, cranes, etc
  Limited number of entities, capacity of transporters
    Like a Resource, except moveable
  Conveyors (Normally unidirectional)
    Belts, hook lines, escalators
    Usually limited space on conveyor, speed
    Non-accumulating vs. accumulating

## Slide 5: Model 8-1: Small Manufacturing System with Resource-Constrained Transfers
Upload (Model 7-1)
  Assumed all transfer times = 2 minutes
  No limit on number of parts in transit at a time
Change– no more than 2 parts can be in motion at a given time
  If other parts are ready to go, they must wait until there’s room to go
Model via existing constructs
  Model; imagine a road with
    Limited number of Units that can seize the road (resource) at beginning of trip
    Release it at end of trip

## Slide 6: Changes to Model 7-1
Replace Route with Leave (Adv. Transfer Panel)
  Transfer out : Seize Resource (Transfer)
Replace Station modules with Enter modules (Adv.Transfer panel)
  Defines the Station
  Transfer In: Release Transfer resource
Run model compare with 7-1 slight changes in WIP and Cycle Times

## Slide 7: Transporter Concepts
Entity is ready to move from point A to Point B, it needs to be “picked up” and moved
Use Transporters — “moveable” resources
Activities: Request, Transport, Free
  Transporter Selection Rule: If > 1 transporter is available when Requesting
  When freed and > 1 entity is waiting: Priorities, closest one
Two types of Transporters
  Free-Path (we’ll do)
    Travel time depends only on velocity, distance
    Ignore “traffic jams” and their resulting delays
  Guided (won’t do)
    AGVs, intersections, etc.

## Slide 8: The Small Manufacturing System with Transporters
There are two carts for transporting parts
  A cart can carry one part at a time
  Carts move at 50 feet/minute
    Will need to specify accurate distances between Stations
  It takes 0.25 minute to load part on a cart, 0.25 minute to unload it from a cart
Modify Model 8-1 to Model 8-2

## Slide 9: The Small Manufacturing System with Transporters (cont’d.) 8-2
Create Transporter in Transporter data module (Advanced transfer panel)
  Name = Cart, Capacity = 2, Velocity = 50
  Default the Distance Set (later), Units = Per Minute, Initial Positions
    Mind the units
    Animation picture for Cart Transporter
  Transporter button (Animate Transfer toolbar)
  Identifier = Cart, pictures for Idle, Busy, Inactive states

## Slide 10: The Small Manufacturing System with Transporters (cont’d.)
Request a Cart – modify existing Leave modules
  Delay = 0.25 Minute for load time
  Transfer Out = Request Transporter
  Transporter Name = Cart
  Selection Rule = Smallest Distance
    Applies when > 1 transporter is available
    Others: Cyclic, Random, Preferred Order, Largest Distance
    Save Attribute = Cart #
    Connect Type = Transport
    Move Time disappears … determined by Velocity, Distances (later)
  Station Type = Sequence
Instead of Leave: Request-Delay-Transport
  More complex, more flexible – book has details, examples

## Slide 11: The Small Manufacturing System with Transporters (cont’d.)
Free the Cart – modify existing Enter modules
  Delay = 0.25 Minute for unload time
  Transfer In = Free Transporter
  Transporter Name = Cart
  Unit Number = Cart # attribute of part entity

## Slide 12: Distances for Transporters
Define contents of Distance Set Cart.Distance
Distances (in feet) moved by parts:
  Blank cells: part movements that don’t occur
Enter these data in Distance data module (Advanced Transfer panel)
  Name = Cart.Distance
  Stations button, add 11 rows with Beginning Station, Ending Station, Distance for above data
  Direction is implied; could be asymmetric
Units!!

## Slide 13: Animating Transporter Movement
Add distances to animation
Delete all the old Route Path animation objects
  But leave the Station animations
Add animated transporter distances with Distance button , Animate Transfer toolbar
  Dialog, placement similar to Route Paths
  Identifier = Cart.Distance
  Click in Beginning Station marker, intermediate clicks, Ending Station marker
  Options for Rotate, Flip
  Grid, Snap to help place animated transporter distances

## Slide 14: Parking Areas for Transporters
Animate transporters when they’re free
Parking button , Animate Transfer toolbar
  Like a Queue animation – Point vs. Line, Shift, Rotate
  Cursor becomes cross hairs, click near lower left of Station marker to start, click for first Point or head of Line
  More clicks for more Points (double-click to end), or second click to end Line
  Want enough points/space for all transporters (2 here)
  Repeat for all Stations where Transporters could be freed

## Slide 15: More Distances — Empty Transporters
Above Distances incomplete — only for part movements along their sequences
Transporters must also move when empty
  In general, n(n - 1) distances need definition for network with n nodes
more distances to define in Distances data module (not grayed):

## Slide 16: Conveyor concept
Entity is ready to move from point A to Point B, it needs to Access a conveyor, be conveyed then exit.
Requires conveyor segments to be defined.
Activities: Access, Convey, Exit
Two types of Conveyors
  Non-accumulating (we’ll do)
    Starts and stops for Access and Exit
    Spacing between entities traveling on Conveyor constant
  Accumulating (won’t do)
    Never stop moving
    Stopped entity blocks entities arriving at same location
Go to Model 8-4

## Slide 17: Modelling Conveyors
Resource-Constrained transfer;
  Seize, Route and Release
Transporters
  Request, Transport and Free
  Needs Distances to be defined
Conveyors
  Access, Convey and Exit
  Needs Segments to be defined